## Slide 1: Join the Cloud!
Robert Nordmark and Brian Burkhart
Director of Network Services
Assistant Director Network Systems

## Slide 2: Included Services
These services are available to you for no additional cost if you are a customer of the OneNet network.

## Slide 3: Web Hosting
No pre-defined limit on the space or bandwidth used if you're following the AUP
Uses cPanel for straightforward control of site options
The Installatron plugin makes installing many open-source web applications super-easy
www.onenet.net is hosted on cPanel alongside member sites
Web and email hosting for non-Internet access customer is $300

## Slide 4: Email Hosting
Unlimited email accounts
IMAP or POP3 for incoming mail
SMTP for outbound mail
WebMail
  Calendar
  Address Book
438 domains with 140,000 accounts

## Slide 5: Anti-SPAM
Based on an open-source project called Maia Mailguard
Your URL is https://yourdomain/spam
Provides virus and spam detection and quarantine
Per-user sensitivity settings and white/black lists

## Slide 6: Domain Name Service Hosting
You can manage your DNS records through your cPanel account (even if we don’t host your web site)
We can make the DNS changes for you
Free registration of lib.ok.us, k12.ok.us, cc.ok.us, and many others
No cost for .k12.ok.us domains, even if you’re not a OneNet subscriber

## Slide 7: Video Conferencing
Multi-Point high-definition conferencing
Conference Recording
Live Streaming
Mobile client available (PC, Mac, iPad)

## Slide 8: Additional Services
These services are offered on a cost recovery basis. You pay what it costs us to provide the service.

## Slide 9: Storage
Whether you need a good place to keep a copy of your data safe, or if you need primary storage, we probably have a solution
IBM Tivoli Storage Manager
IBM N-Series (NetApp) Storage
SAM-FS

## Slide 10: TEXTEXTEXTEXTEXTEXT
  Traditional server backup
  Client installed on your mission-critical server
  Your data is automatically backed up to our OKC and/or Lawton storage systems
  Cost is $15/50G/year for total space used in the backup system
  One-time $500 setup fee per system covers license costs

## Slide 11: TEXTEXTEXTEXTEXTEXT
Dedicated File Services
  Great for use as a primary file server if you have a larger pipe
N-Series Snapmirror
  Perfect DR backup solution if you're running IBM N-Series or NetApp storage
  Mirror your data to one of OneNet's datacenters

## Slide 12: Colocation
OKC Data Center Colocation
  Redundant 10 Gig connections to OneNet core
  Redundant UPS power with generator backup
  $20 per rack unit per month
Perimeter Technology Center
  Redundant 10 Gig connectivity to OneNet core
  Contact PTC for more information

## Slide 13: Learning Management Systems
  Commercial LMS offerings
  Hosted in OneNet's data center
  Supported by Desire2Learn and Blackboard
  Open-Source LMS
  Can be run on OneNet's shared Web hosting service (free) or on a dedicated VM
  We have members running it both ways
  Forum-based support or commercial support offerings available

## Slide 14: Mail Archiving
Email compliance archiving
  Based on Tangent Datacove
  This software is co-developed with the makers of MailArchiva
  Can be used with or without our email service
  Archives all messages in or out of your domain
  Full text searching of messages and attachments
  Unlimited retention as long as the mailbox archive subscription is current
  Cost is $10 per mailbox per year

## Slide 15: Virtual Infrastructure
Dedicated Virtual Machine
DR Backup (snapmirror to Tulsa) included
VMware High Availability included
ICB needs can be met
Virtual CPUs | RAM | Disk | Annual Cost
1 | 2G | 36G | $600
2 | 4G | 72G | $1100
4 | 8G | 144G | $2100

## Slide 16: Network Virtualization
Robert Nordmark will now discuss our network virtualization offerings.

## Slide 17: What is MPLS?
MPLS stands for “Multi-Protocol Label Switching”
MPLS is best summarized as a “Layer 2.5 Networking Protocol”
OneNet offers several types of network virtualization:
Layer 2 VPN’s
  Point to Point
  Point to Multipoint
Layer 3 VPN

## Slide 18: Layer 2 VPNs
Layer 2 Pseudowire or VLL (Virtual Leased Line)
An emulated layer-2 point-to-point circuit, delivered over MPLS
Can be used to interconnect two different types of media:
  For example, Ethernet to T1
Useful for migrating legacy transport to an MPLS network
Completely Circuit Technology Agnostic
Scales to extremely large deployments

## Slide 20: Layer 2 VPLS
VPLS (Virtual Private LAN Service)
Creates an Ethernet multipoint switching service over MPLS
Used to link a large number of customer endpoints in a common broadcast
domain
Avoids the need to provision a full mesh of L2 circuits
Emulates the basic functions of a layer 2 switch:
  Unknown unicast flooding
  Mac learning
  Broadcasts
Typically load-balancing friendly since the L2 Ethernet headers are examined and used, unlike L2 pseudowires where they are passed transparently

## Slide 22: Layer 3 VPN
An IP-based VPN
Networks build virtual routing domains (VRFs) on their edge routers
Customers are placed within a VRF, and exchange routes with the OneNet router in a protected routing-instance.
Can support complex topologies and interconnect many sites
But can add a significant load to the service provider infrastructure
Typically seen in more enterprise environments
Signaled via BGP within the OneNet network

## Slide 24: OneNet Virtualized Data Center
IBGP / OSPF
MC-LAG
2
2

## Slide 27: OneNet Class Of Service
Expedited forwarding (EF)—Provides a low loss, low latency, low jitter, assured bandwidth, end-to-end service.
Assured forwarding (AF)—Provides a group of values you can define and includes four subclasses: AF1, AF2, AF3, and AF4, each with three drop probabilities: low, medium, and high.
Best effort (BE)—Provides no service profile. For the BE forwarding class, loss priority is typically not carried in a class-of-service (CoS) value, and random early detection (RED) drop profiles are more aggressive.
Network Control (NC)—This class is typically high priority because it supports protocol control.
Scavenger Class (SC) — Lowest Priority on traffic, If bandwidth is close to full packets are dropped.

## Slide 28: Content Filtering Services
OneNet will provide a fast, economical, secure, and flexible web content filtering solution.
Centralized Solution –
OneNet will work with you to forward all your web traffic to one of OneNet’s centralized web filtering server.
Decentralized Solution –
OneNet will provide on-site customer premise eqipment. This solution will provide the customer more granularity in the web filtering.

## Slide 29: QUESTIONS?